## Slide 1: Bitslicing using Small-scale Hierarchical Floorplanning
Evan Vaughan

## Slide 2: Review
Get RTL Compilier and SoC Encounter to place & route a bitsliced datapath
Began by modifying/reducing libraries
  Modify>synthesize>P&R
Very time consuming and no good results.

## Slide 3: Since the last time…
Original approach involved far too much custom design
  Abandoned that.
Focus has shifted to floorplanning
Use hierarchical design methodologies to floorplan

## Slide 4: Hierarchical Design
Meant for large-scale designs
  By default, Encounter only makes it available for larger designs
Breaks design into manageable pieces when floorplanning
Allows for parallel design of blocks

## Slide 5: Approach
First must make a hierarchical design
  Original Kogge-Stone verilog completely flat
Modified verilog to
make overall
design hierarchical

## Slide 6: Synthesis Results
Flat Design
Hierarchical Design

## Slide 7: Place & Route
Hierarchical design yields no difference in P&R

## Slide 8: Hierarchical Floorplanning
Uses partitions, modules, groups, fences, etc…
Fence allows user to define spaces where standard cells will be placed
  Can specify modules as fences
Specify each bit module as a fence
  Place fences in core as bitslices
  Place cells in fences
Encounter wasn’t showing my bits as modules

## Slide 9: Modules

## Slide 10: Black Box Flow
Defining black boxes creates instances of the modules
Can place modules by hand then place black boxes (Place>Standard Cells)
Remove black boxes (unspecifyBlackBox –keepPtn)
  Removes black boxes but leaves fence behind
  Can then place standard cells within module fences.

## Slide 11: Placement

## Slide 12: Problems
Kind of a hack
  Can’t unspecifyBlackBox from GUI
  Multiple placements
Works fine as script but cumbersome in the GUI
Can ignore Black Box flow and directly specify fences in a script or in terminal
  Still no way for GUI-based flow
  Fences do not show up in floorplan view

## Slide 13: GUI-based Flow
By default, Encounter requires >100 cells for a module to be displayed after import.
  Design>Preferences>Display Min. Floorplan Module Size to change this.
  Alternatively “setPreference MinFPModuleSize 0” in a script/terminal
Can easily place & resize modules into the core area
  Define them as fences
  Place standard cells

## Slide 14: Scripting
Very easily implemented as a script
Fences prevent cells from moving outside of assigned rows
  Optimization can be run without destroying bitslice
Easily integrated into any flow

## Slide 15: Results

## Slide 16: Final Layout (Pre-optimization)

## Slide 17: Post-optimization (Timing)

## Slide 18: Final Layout (Post-optimization)

## Slide 19: What I’ve Learned
No previous ASIC design
  Scripting
  Synthesis
  Place & Route
  Verilog
Hierarchical Design methodologies

## Slide 20: Questions?